## Slide 1
MAIB AI 218 · AI IN OPERATIONS
RAQIB · رقيب The watcher on the floor
01
A vision-driven operations control room for supermarket floors.
Same engine, factory profile: MUSHRIF for the Greenlam pilot.
Krishna Mathur · github.com/krish2105/RAQIB-AI-in-Operations
Notes: Open with the name: RAQIB means the watcher. Existing cameras, an edge box, an agent that explains itself. Krishna Mathur, Term 4 deployed MVP.

## Slide 2
THE PROBLEM
Every store has forty cameras and nobody watching them
02
Queues longer than three customers drive walk-outs. Shelf gaps cost ~4% of sales (Gruen et al., 2002).
Both are counted by hand, by mystery shoppers, or not at all.
The gap is not sensing. It is turning what the camera sees into a decision inside the shift.
Notes: One picture: a checkout queue and an empty shelf. Queues over three cause walk-outs; out-of-stocks cost about 4% of sales. Cameras record both and act on neither.

## Slide 3
WHAT RAQIB DOES
Sees · Learns · Acts · Explains
03
Sees — person tracks, queue zones, checkout dwell, shelf empty ratio
Learns — M/M/c utilisation, next-24 h forecast, staffing integer program
Acts — templated alerts, restock work orders, proposals to open a till (only if ρ > 0.85)
Explains — every action carries the rule id, the confidence, and a written rationale
Notes: Four verbs. Sees: footfall, queues, checkout dwell, shelf gaps. Learns: queueing model, forecast, staffing plan. Acts: alerts, restock tasks, proposals for tills. Explains: rule, confidence, rationale on every action.

## Slide 4
ARCHITECTURE
Rules on the edge, judgement in the cloud, humans on the floor
04
edge/ capture → blur every head → YOLO26n ⇄ RT-DETR → ByteTrack → zones → deterministic rules → SQLite → idempotent sync
cloud/ events · SSE · M/M/c · OSA · forecast · MILP · agent: backend → Policy → 7 allow-listed tools → Greenlam tracker
web/ the 24-hour tape · KPIs · 3D floor · event clip + decision · approve/reject · forecast · report EN/HI/AR
Notes: Edge: capture, blur faces, detect, track, rules, SQLite, sync. Cloud: events, analytics, bounded agent behind a policy. Web: the tape, KPIs, 3D floor, actions. Detector is behind an adapter; YOLO26 swaps for RT-DETR with one flag.

## Slide 5
LIVE DEMO
raqib-orcin.vercel.app
05
1 · Dashboard: the tape, KPIs, 3D floor pulsing where events land
2 · Click a tick: clip (faces blurred), confidence, rule R10, agent decision
3 · Actions: approve 'open till 2' → Executed; restock work orders raised autonomously
4 · Forecast and staffing plan · 5 · Weekly report, print to PDF
Notes: Grader path in under ten minutes: dashboard → tape tick → event clip and decision → approve a proposal → executed and audited → forecast → report. QR on this slide when deployed.

## Slide 6
DETECTION
Same pipeline, two detectors, one flag
06
8.9 ms
YOLO26n median latency per frame (MPS)
30.5 fps
end-to-end: detect, track, blur, rules, store
56.1 ms
frame → event, p95
Notes: Adapter pattern exists for licensing: Ultralytics is AGPL; RT-DETR architecture is Apache. Numbers from edge_eval.json on the M4 Pro.

## Slide 7
QUEUE MODEL VS OBSERVED
Peak utilisation ρ 0.95 · service level 98.9%
07
λ from entrance ticks per 15 min
μ ≈ 38/h per till, estimated from video
Observed W_q = queue length / λ (Little)
Target: ρ ≤ 0.85, queue ≤ 3 in 90% of slots
Notes: M/M/c with lambda from footfall ticks and mu from checkout dwell on video. The observed W_q via Little's law sits on the same chart as the model; the gap is the point, not a caveat.

## Slide 8
FORECAST VS BASELINE
11.7% better than seasonal naive
08
4.341
MAE, gradient boosting
4.917
MAE, seasonal naive
Notes: Gradient boosting versus same-hour-last-week. MAE 4.341 vs 4.917, MAPE 16.4%. Honest caveat: this is on the labelled simulator; real data with promotions and weather should widen the margin.

## Slide 9
WORKFORCE OPTIMISATION
24.25 staff-hours instead of 36.0
09
11.75 h
saved per day vs three tills all day
17.2%
less customer wait with proposals applied
Notes: Integer program: minimise tills per slot subject to rho ≤ 0.85. Saves 11.75 staff-hours a day; wait time before/after with proposals applied: 17.2% reduction.

## Slide 10
AGENT GOVERNANCE
Bounded autonomy, not blind autonomy
10
Autonomous: alert (templates), restock/work order ≤ sev 2, log downtime, escalate on sev 3, ask for review < 0.6 confidence
Proposal: open till (must cite ρ > 0.85), staffing change, maintenance window
Policy cannot be bypassed by either backend (dry-run or Claude)
Every call validated and logged: input, output, latency, cost
This week: 1 actions · 1 calls · 0 failed · $0.0
Notes: Seven allow-listed tools with strict schemas. Severity 3 always escalates and cannot be downgraded. One work order per machine per 4 hours. Proposals need a human. Seeded week: 1 actions, 1 tool calls, 0 failed, $0.0 model cost.

## Slide 11
BUSINESS CASE
One Dubai hypermarket, 90 days
11
Weeks 1–4 · one entrance, one checkout bank, three shelves · gate: false alerts < 5/camera/day, approval ≥ 60%
Weeks 5–8 · all tills, POS import for μ, staffing plan into rosters · gate: service level ≥ 90%, forecast ≥ 20% better on real data
Weeks 9–13 · aisle shelves, second store · gate: OSA ≥ 98%, < USD 150/store/month
Factory profile today: compliance 100.0%, 3.0 min downtime, 1 breach in 24 h on the Greenlam demo site
Notes: Pilot on existing cameras and an owned edge box. Software under USD 50 a month. Gates: false alerts under 5 per camera per day, approval rate over 60%, then service level 90% and OSA 98%. MUSHRIF factory profile shares the engine.

## Slide 12
LIMITATIONS · NEXT STEPS · THANK YOU
Data is the risk. Trust is the product.
12
Public clips, not a store · μ estimated from video · 21-day labelled simulator · COCO weights, PPE mAP not measured · AGPL detector
Next: POS import · two hours of labelled site footage · planogram check · digital-twin playback · 24-hour unattended soak
شكرًا · धन्यवाद · Thank you
Notes: Say the limits plainly: public clips not a store; mu from video not POS; simulator history; AGPL. Next: POS import, labelled site footage, planogram checks, digital-twin playback, 24-hour soak. Thank you.